1995 CSI SECTION 08160 SLIDING METAL DOORS

2004 CSI SECTION 08 32 13 SLIDING ALUMINUM - FRAMED GLASS DOOR

(Window Walls/Ribbon Walls)

PART 1 General

- Summary

  - Section includes:

    - Sliding Metal Doors

  - Related Sections:

- References

  - American Architectural Manufacturers Association (AAMA)

  - American Society for Testing and Materials (ASTM)

  - National Accreditation & management Institute (NAMI)

  - National Wood Window & Door Association (NWWDA)

- System Description

  - General: In addition to requirements shown or specified, comply with:

    - Applicable provisions of AAMA Windows and Sliding Glass Doors Manual for design, materials, fabrication and installation of component parts.

  - Design Requirements: Arcadia ULT5000IP Series SGD-DP -/+ 70 psf -Small & Large Missile Impact using 1-1/16” Laminated Insulated Impact Glass.  Arcadia ULT5000IP NI Series SGD –using 1” IG temp Glass -DP -/+ 60 psf ( @ 8’6” tall panels) –Higher DP performance pressures available based on door size and configurations.

  - 2 panel configuration only tested.

Sliding Glass Doors 4 ½” (5 ¼” depth w/screen).

  - Performance Requirements: Each assembly shall be tested by a recognized testing laboratory or agency in accordance with specified test methods.

    - Conformance to & ASTM E1886/1996                   (Small Missile & Large Missile) & AAMA/WDMA/CSA 101

NFRC tested for:

-NFRC 100-2004 for fenestration U factors.

-NFRC 200-2004 for fenestration solar heat gain coefficients & visible transmittance at normal incidence.

-NFRC 500-2004 for fenestration condensation resistance values.

      - Air Infiltration: Accordance with ASTM E 283.

      - Water Resistance: Accordance with ASTM E 331.

- Quality Assurance

  - Single Source Responsibility:

    - Obtain entrances, storefronts, ribbon walls, window walls, curtain walls, window systems, and finish through one source from a single manufacturer.

  - Provide test reports from AAMA & NFRC accredited laboratories certifying the performances as specified in 1.03.

- Warranty

- Warranted against failure and/or deterioration of metals due to manufacturing process for a period of one (1) year.

PART 2 Products

- Manufacturers

  - Acceptable Manufacturers:

    - Arcadia Architectural Products, Inc., 60 Bonner Street, Stamford, CT. 203-316-8000, fax 203-316-8200.

  - Acceptable Products:

    - Arcadia Series ULT5000IP Impact (Small & Large missile impact) – Arcadia Series ULT5000IP-NI Sliding Glass Doors - 4 ½” (5 ¼” depth w/screen).

- Materials

  - All doors shall be fabricated from aluminum extrusions of 6063-T6 alloy and temper with a minimum wall thickness of 0.100” for the sill member and a minimum of 0.072” for all other members, including frame & sash. The aluminum shall be free of defects which impair strength and appearance.

All panel members will have a minimum .625” glass penetration (ULT5000IP Small & Large Missile) .625” glass penetration into the aluminum to provide extra protection against de-glazing or blow out in high wind conditions.

  - Component parts and accessories shall be of aluminum alloy, stainless steel or non-metallic materials, which will neither deteriorate nor promote corrosion.

  - Sill shall have a full length roll-formed 0.028” thick stainless steel track cap. Sill shall have a full-length roll-formed 0.028” thick stainless steel track cap.

  - Operable sash shall be equipped with two stainless steel tandem ball bearing roller assemblies.

  - Fully Stainless Steel Locking device Adams-Rite maximum security lock MS+1950 with hook bolt standard.

  - Operating panels shall have an extruded 3/4” diameter 8” O.C. aluminum wire pull handle set in either clear or black anodize finish – other colors available.

  - Fixed and/or sliding sash members shall be constructed to allow for either factory or field glazing. Sash glazing shall be “Dry” & accomplished using a “marine” style reusable, wraparound black flexible polyvinyl chloride (PVC) or EPDM material per commercial standard CS230-60 without the need for separate glazing beads or putty style bedding compounds. The glazing channel shall be provided with the unit for 1-1/16” Insulated Laminated Glass.

  - All assembly and installation screws shall be 18-8 or 410 stainless steel.

  - Screens - Optional – Shall be Interior Sliding made of extruded aluminum frame and screened with 18 x 16 fiberglass mesh. (5 ¼” Frame Depth Overall)

- Finish

  - Finish all exposed areas of aluminum and components as indicated (excluding hardware):

    - Clear Anodized Class 1 (215R1-0.7 mils thick) meeting AAMA 611.89

    - Dark Bronze Anodized Class 1 (0.7 mils thick) meeting AAMA 611.89

    - Custom colors in a baked-on enamel or Duranar finish are also available – AAMA 2604.98 and AAMA 2605.98 subject to minimum square footage requirements.

- Fabrication

  - Jambs are cut and square butt joined to sill & head to ensure a weather resistant seal & must be back caulker.

PART 3 Execution

- Examinations

  - Examine conditions and verify substrate conditions are acceptable for product installation.

- Installation

  - Install in accordance with approved shop drawings and manufacturers installation instructions.

- Field Quality Control

- Contractor’s responsibility to make all necessary final adjustments to attain normal operation of each door and its mechanical hardware.

END OF SECTION

# Text boxes

(or)

(or)